## Slide 1: Digital Systems CS 260
Maurice McGlashan-Powell
Lecture II

## Slide 3: Generic Computer
Block Diagram
CPU
  Central Processing Unit
FPU
  Floating Point Unit
MMU
  Memory Management Unit
Internal Cache
External Cache
RAM – Random Access Memory
  On board Memory
Buss Interface
  Interface various components (CPU, RAM, Drive controller, etc

## Slide 4: Generic Computer
Memory
  Stores program, input and output and intermediate data
Data path
  Performs arithmetic and data processing operation specified by program
Control Unit
  Supervise flow of information between units
CPU – Central Processing Unit
  Data path combined with control unit
Input/Output (IO)
  Input
    Program and data transferred to memory
      Usually a keyboard
    Output
      Displays results of computation
        Usually LCD or other monitor

## Slide 5: Other I/O Devices
CD-ROMs
DVD
Scanners
Printers

## Slide 6: Micro computers, Micro controllers, DSP and Embedded systems
Small computer embedded into every day equipment and often not apparent
Micro controllers, DSP and other embedded system controls:
  Temperature, speed, air pressure, etc

## Slide 7: Micro computers, Micro controllers, DSP and Embedded systems
Small computer embedded into every day equipment and often not apparent
Micro controllers, DSP and other embedded system controls:
  Temperature, speed, air pressure, etc

## Slide 8: Binary Numbers
Binary Number system
  Base 2 system with two digits or bits (0 and 1)
    A bit is a binary digit
  Example
  Subscript (2) for the binary number (11010) indicates the base of the number (base 2)
  Subscript (10) of the decimal number 26 indicates base (10)
Assign 2.1
  Show that the decimal (base 10) equivalent of the binary number 110101.11 is equal to 53.75

## Slide 9: Powers of 2 Table
The first 24 numbers obtained from 2 to the power of n
Is referred to as K or Kilo
is referred to as M or Mega
is referred to as G or Giga
is referred to as T or Tera
4K =
4k
Assign 2.2:
What is 16 M equal to?

## Slide 10: Conversion of decimal numbers to Binary
Conversion of a decimal number is achieved by sucesivly subtracting powers of 2 from the decimal number
To convert decimal number N to Binary
  Find the greatest number that is a power of 2 that when it is subtracted from N yield a positive difference
    Call the difference N1
  Find the greatest number that is a power of 2 that when if is subtracted from N1 produces a positive difference N2
    Repeat this until the difference is Zero
Example: Convert decimal 625 to binary
625-512 = 113 = N1 , 512 =
113 – 64 = 49 = N2 , 64 =
49 – 32 = 17 = N3 , 32 =
17 – 16 = 1 = N4 , 16 =
1 – 1 = 0 = N5 , 1 =
So 625 =

## Slide 11: Boolean Algebra
Branch of mathematics that describes the operational properties of digital circuits
  The mathematical notation that specifies the operation of each logic gates and is used to analyze and design logic circuits
Binary Logic
  Relates to binary variables which have two discrete values and the operation of mathematical logic that applies to these variables
Binary Variables (A,B,C, X,Y,Z) are assigned to values of 0 or 1
Logical Operations
  AND
    Inputs binary variables A and B
    Output A.B = 1 only if A =1 and B = 1
  OR
    Input variables A and B
    Output A +B = 1 if either A =1 or B = 1 or both A and B =1
  NOT
    Input variable A
    Output = 1 if A =0
    Output =0 if A =1

## Slide 12: Logical Operators
AND
  Represented by dot or no operator at all
  Z = A●B or Z = AB
OR
  Represented by “ +”
    Z = A or B
      Z = 1 (True) if and only if
        X = 1 or Y = 1 or X = 1 and Y = 1
      Z = 0 if
        X = 0 and Y = 0

## Slide 13: Binary Logic
Binary Logic resembles arithmetic
  The logical operators AND and OR are similar to multiplication and addition
  BUT
    DO NOT confuse binary with binary arithmetic
    Arithmetic variables can have many digits
    Logical variables and ONLY have values of 0 or 1
Binary Logic Equation that defines the logical OR operator
    0 + 0 = 0
      If the inputs to and OR gate are A = 0 and B = 0
        The output is 0
    0 + 1 = 1
      If the input to an OR gate is A = 0 and B = 1
        The output is 1 (true)
    1 + 1 = 1
      If the input A =1 and B = 1
        The output is 1 (true)
The binary logical equation that defines the logical AND operator
    ● 0 = 1
      If input A = 0 and input B = 0
        The output is 0
    0 ● 1 = 0
      If input A = 0 and B =1
        Output = 0
    1 ● 0 = 0
      If input A = 1 and input B = 0
        Output = 0
    1 ● 1 = 1
      Only if input A = 1 and B = 1
      Output = 1

## Slide 14: Truth tables for Logical Operators AND, OR and NOT
  AND operator
  OR operator
  NOT operator
X | Y | Z = X + Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
X | Z =
0 | 1
1 | 0
X | 
0 | 1
1 | 0

## Slide 15: Logic Gates
X
Y
Z = X●Y
Logic gates
  Electronic circuits that operates on one or more input signal to produce an output signal
Graphical symbols for logic Gates
AND gate
OR gate
NOT gate or Inverter
Type equation here.
Z =
X
Z = X + Y

## Slide 16: Logical Gates (continued)
Two input signal to AND or OR gates hae four possible combination
  00, 01, 10, or 11
Timing Diagram for AND and OR gate
X | 0 | 0 | 1 | 1
Y | 0 | 1 | 0 | 1
X●Y | 0 | 0 | 0 | 1
OR gate
X + Y | 0 | 1 | 1 | 1
AND gate
Time

## Slide 17: Boolean Algebra
Algebra relating to binary variables and logic operations
Binary Variables
  Represented by letters and the basic logic Operators (AND, OR and NOT)
Boolean expressions
  Algebraic expressions formed by using binary variables, constants (0, 1), the basic logic operators symbols and parenthesis
Boolean Functions
  Described by a Boolean equation consisting of a binary variable identifying the function followed by a equal sign and a Boolean expression

## Slide 18: Boolean Function – The Power Window
Electronic logic for Lowering the Power Window of a Car
The Boolean Function
  + A
    If D=1, X = 1 or A = 1
      Then L = 1
The window is lowered by a motor and lever mechanism
L = 1
  Window Motor is Powered (on) to turn in the direction to lower the window
L = 0
  Motor is Not powered to lowere the window
D = 1
  A request to lower the window is issued (by pressing a button or Switch)
D = 0
  Lowering action is Not requested

## Slide 19: Boolean Function – The Power Window
The Boolean Function
  + A
X
  The output of a limit
X = 1
  The window is at its lower limit (fully down)
X = 0
  Window is Not at lower limit (Not fully down)
A – Signal generated by timing logic from D and X
If D = 1 (on) for a least half a second
  Then A = 1 and remains 1 until X =1
  X = 1 when the window is fully down (limit)
If D = 1 (Request to lower Window) for less than a half second
  Then A = 0 and there is no automatic lowering
So, If the driver presses the switch for more than ½ second the window lowers automatically to the lower limit of fully down

## Slide 20: Boolean Function – The Power Window
and A of the Boolean expression are called the terms of the expression + A
Function L = 1
  If term = 1
  OR term A = 1
Else L = 0
The complement operation of is then X = 0
  Therefore
  L== 1 if D = 1 and X = 0 or if A = 1
The equation expression + A
  States that the window will be lowered if the window is not fully lowerd (X = 0) and the switch is pushed (D = 1) OR if the window if to be lowered automatically to a fully down position (A = 1)

## Slide 21: Boolean Equations
Boolean Equations
  Expresses the logical relationship between binary variables
  Evaluated by the determining of the binary values of the expression for all possible combination of values for the variables
A Boolean Function can be represented by a truth table
Truth Table for a Boolean function
  A list of all combinations of 1`s and 0`s that can be assigned to the binary variables and a lit that shows the value of the function for each binary combination

## Slide 22: Truth Table for a Boolean Function
The truth table for the Boolean Function + A
The number of rows in a truth table is
  Where n = the number of variables in the function
There are 8 possible binary combination for the function L
D | X | A | L
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 1 | 0 | 0
1 | 1 | 1 | 1

## Slide 23: Transformation of Algebraic expression for a Boolean Function
An algebraic expression for a Boolean function can be terraformed to a circuit diagram composed of logic gates that implement the function
Logic Circuit Diagram for Function + A
D
X
Z = X●Y
A
A
L

## Slide 24: Simplification of Boolean Expressions
Boolean expressions can be simplified using Boolean Algebraic rules
  This reduces the number of gates
Basic Identities of Boolean Algebra

## Slide 25: Boolean Identities (continued)
Boolean algebra identities 10 through 14
  Normal algebraic properties
Dual of a Boolean algebra expression
  Obtained by interchanging Boolean operator OR and AND
  and by replacing 1’s with 0’s and 0’s with 1’s
Equation from on side of the table of Boolean algebraic identities (odd numbered identities) can be used to generate the expressions on the other side (even numbered identities) by taking the dual of that expression

## Slide 26: Boolean Identities (continued)
Any expression can be substituted for X in the identity table
  Ex1.
    Using identity X + 1 = 1
    Let X = 0
      Then 0 + 1 = 1
  Ex2
    Using identity X + 1 = 1
    Let X = AB + C
    Then
    (AB + C) + 1 = 1
Identity 15 is the dual of identity 14
    Identity 15 does NOT correspond to ordinary algebraic distribution law

## Slide 27: Boolean Identities (continued)
Each variable in the Boolean algebraic identity table can be replaced by a Boolean algebraic expression
For the expression
  (A + B)(A + CD)
  Let X = A, Y = B and Z = CD
Using the second distributive law (identity # 15) then
  A = BCD = (A = B)(A = CD)

## Slide 28: Boolean Identities (continued)
DeMorgans Theorem
  Used to obtain the complement of a expression and the complement of the corresponding function
    Remember
      The complement of 1 is 0
      The complement of X is

## Slide 29: Boolean Identities (continued)
Evaluating the truth table for DeMorgans Theorem (part a)
  Evaluate the complement of X and Y first
  This Yields
Then evaluate the AND function
For part b
Evaluate the OR operator first
Then the complement
The general DeMorgan expression
=
De Morgan’s Theorem Changes an expression from OR to AND and from AND to OR

## Slide 30: Boolean Algebraic Manipulation
Boolean Algebra is used to simplify digital circuits
Consider the Boolean Expression
Implementing this expression in terms of Gates

## Slide 31: Boolean Algebraic Manipulation
Simplification of the Boolean Expression
Using the Boolean Algebraic identities number 14 – X(Y = Z = XY + XZ
And substituting Y
Y(Z +
Using identity 7: = 1
yield:
Using identity 2
This expression now has only 2 terms and the resulting number of gates is greatly reduced
Implementing this expression in terms of Gates

## Slide 32: The Truth Table for The Boolean expression Fa and Fb
Fa = Z
Fb =
Fa = Fb therefore the circuits are Equivalent

## Slide 33: Implementing a Boolean Equation With Gates
Each Term is implemented with a gate
The inputs to the logic gates are the variables of the Boolean expression (X, Y,Z, A, B, C etc)
Literal
  A single variable within a term
Reducing the number of terms and variable in a Boolean expression reduces the complexity of the circuit

## Slide 34: Tools for reducing Boolean Expressions
Using the identity table reduces Boolean expressions
The following expression along with the Identity table are also useful for reducing the Boolean expressions

## Slide 35: Assignment

## Slide 36: Assignment

## Slide 37: Assignment